# CHAPTER 2.  General Requirements

### 2.1 	Planning/Design

2.1.1	The planning, design and documentation of landscape work shall be such that all bylaws, legislation, applicable codes, regulations and guidelines, including this Guideline, can be met during the construction and maintenance phases and upon completion of the Work.

2.1.2	The potential for retaining existing site elements should be thoroughly examined during the initial site planning.  Preliminary planning and subsequent design development should include, and be based on the findings of a review of the existing site elements by a qualified professional, such as a Registered Landscape Architect or an ISA Certified Arborist.

2.1.3	The Owner shall be responsible for ensuring that the provisions of 2.1.1 are met, and shall ensure that its consultants, agents and contractors for the Work, comply with all bylaws, legislation, applicable codes, regulations and guidelines, including this Guideline.

2.1.4	Professional consultants having expertise appropriate to the needs of the project should be engaged in the planning and designing of the work.

### 2.2 	Working Documents

2.2.1	Existing conditions and new work shall be adequately and accurately described in a set of working documents and specifications to be provided to the Contractor and the Authority/Owner (see General, 1.2, Administration Recommendations).

2.2.2	Working documents shall include both drawings and specifications.

2.2.3	Specifications may be included as part of the drawings or may be bound separately.

2.2.4	Specifications shall be specific to the requirements of the project, stipulating products, execution by description or by reference to recognized guidelines, performance criteria and or classes of execution.

2.2.5	Specifications for the project should conform to or exceed this Guideline.  (Listing of Specification Numbers, See Appendix “C”)

# 2.2.6	Landscape Construction Documents may be divided into separate drawings, varying upon the scope and degree of complexity of the project or owner, and should minimally contain or outline the following:

.1	Site Plan

.1	A scaled drawing that should include:

.1	Locations of legal property lines

.2	Any easements in force

.3	Center lines of adjacent streets

.4	Compass directions

.5	Fixed structures

# .2	Landscape Plan

.1	The landscape plan maybe incorporated with the site plan or submitted as a separate document.

.2	A scaled drawing including all pertinent features of the site, both existing and proposed.

.3	Enlarged portions of the plan may be included for intricate or generalized construction details.

.4	Plant materials list or hardscape specifications maybe included as sidebars or boxes

.5	The location of the following features should be included:

.1	Existing vegetation/trees to be retained or removed

.2	Existing natural features

.3	Location and type of protection measures for the existing vegetation/trees to be retained

.4	Elevations at the base of trees to remain

.5	All proposed plant material, planting beds and sodded areas

.6	Plant list showing index, type, size, quantity, species, spacing, etc.

.7	Composition of all hard surfaced areas (driveway, walks)

.8	Height and materials of all fences, screen walls and retaining walls, etc.

.9	Storm water management landscape features

.10	Above and below ground utilities including lighting facilities

.11	Proposed grades, existing grades along the property lines

.12	Any other landscape element that contributes to site development.

# .3	Demolition Plan

A scaled plan should include existing features or elements that are or/not part of the final design.

# .4	Grading Plan

.1	Map of existing and proposed, changes to the contours.

.2	The grading plan is used to delineate elevations and drainage patterns.  It also forms the basis of erosion, sediment and storm water control plans.

.3	A scaled drawing should include:

.1	Indications of benchmark location(s) and elevation(s)

.2	Elevations of permanent features on the property

.3	Alterations to existing grade

.4	Final grading plan

.5	Site boundaries

.6	Existing landform contours with a benchmark to indicate the base for the elevations shown

.7	Existing site features

.8	Proposed site structures

.9	Degree and length of finished slopes

.10	Drainage areas and patterns

.11	Erosion and siltation control plans

.12	Existing and proposed slopes/terraces or retaining walls

.13	Location of the slope, cut and fill areas and finished elevations

# .5	Planting Plan

.1	The planting plan shows the location and types of proposed plant material in the project as noted in the plant schedule.

.2	The plant schedule should contain the following elements, if applicable:

.3	Common and botanical names including:

.1	Plant size

.1	Height

.2	Width

.3	Caliper

.2	Condition

.1	Container grown (specify size)

.2	Balled and burlapped (field-dug)

.3	Bare-root

.3	Form

.1	Guideline (single trunk)

.2	Multi-trunk

.3	Foliated to ground

.4	Grafted

.5	Dwarf

.6	Weeping

.7	Columnar

.4	Quantities

.1	Total number of each plant type, container size and spacing

.5	Notes or special requirements

# .6	Irrigation Plan

.1	An irrigation plan is a schematic representation of the equipment and materials necessary for the preservation or installation of the irrigation system.

.2	Depicting irrigation elements should use consistent symbols.  The symbols should be listed and described in an irrigation schedule or legend as well as cross-referenced to the appropriate irrigation details.

.3	A properly designed irrigation plan should identify: location, specifications, quantities, installation information of the following irrigation components and features:

.1	Water source and point-of-connection

.2	Electrical power source

.3	Electric wires for timers and controls

.4	Meter (if required)

.5	Emergency shutoff valve(s)

.6	Irrigation electronic and manual controller

.7	Sprinkler heads, pipes, and valves

.8	System drain valves: Automatic and manual

.9	Back-Flow prevention device

.10	Pressure regulators

.11	Drip emitters

.12	Filters

.13	Moisture sensor

# .7	Construction Details

.1	Generally, on larger jobs, construction details are included separately from the landscape plan.

.2	Construction details provide specific information for executing a landscape project.

.3	Examples of landscape elements that should be scaled and detailed:

.1	Pavements

.2	Planting pits

.3	Retaining walls

.4	Paver stones

.5	Irrigation system components

.6	Berms

.7	Swales

.8	Benches

.9	Fences

2.2.7	Specifications:

.1	Control the quality and direct the method of construction for a landscape project.

.2	Take precedence over all drawings and notes and are crucial to the execution of a project.

.3	Include technical data to support the information contained in the drawings.

## 2.2.8	Contract

.1	This Guideline sets out to define the fundamental components for a contract for the Landscaping industry.  These fundamentals do not in any manner detail the specifics or legal vernaculars.  These components should be considered when producing documentation.  A lawyer should notarize the resultant document.

.2	The contract is the document that clearly states the expectations and responsibilities of the parties involved in a project and protect each party's rights concerning the project.  The signed contract is a legally binding document.

#### .3	A contract may contain the following sections and information:

.1	Scope of work

.1	All work that is to be performed should be clearly defined. Include the overall scope plus individual aspects such as color, style, and manufacturer.

.2	Landscape plans are generally referred to in the scope of work.

.3	This section includes the Landscape construction plans or maintenance work, plus individual aspects such as planting, grading and site maintenance.

.2	Materials and Equipment

.1	All equipment that will be required to complete the work should be listed.

.2	All materials and products should be identified and specified by name, style, quality, quantity, weight, colour, manufacturer and any other pertinent facts.

.3	Schedule

.1	The duration of the project should be defined.

.2	The workers’ daily working times and days of work should be clearly outlined.

.3	Provisions for any of the numerous factors that can delay a project, such as weather, change orders, and unforeseen circumstances should be addressed.

.4	Insurance

.1	The contract should state the contractor is required to show proof of all the requested insurance, particularly general liability and Workplace Safety Insurance Board coverage for their employees.

.2	The contract should also require the contractor to verify that any subcontractors have their own required valid insurance.

.5	Warranties

All written warranties provided with any equipment or materials used in the project should be noted.

.6	Payment

.1	For large projects a schedule of progress payments is recommended for inclusion in the contract.  The schedule should include the date, amount of each payment or the completion stage of the project required before payment is made.

.2	 A percentage of the final payment or contract price maybe withheld by the owner until all work is satisfactorily completed and sign off by both parties is completed.

# .7	Arbitration

All contracts should contain clauses specifying what form of arbitration should be conducted and by whom if disputes cannot be resolved amicably between owner and contractor.

.8	Miscellaneous

.1	The following are some specific issues to consider addressing in the contract:

.1	Contractors’ operating regulations and parameters pertaining to the site:

.2	Contractual points to verify before submittal to or from the owner or representative:

.3	The first paragraph should state the correct legal names of the parties involved.  For individuals, include full first, middle initials and surname. If applicable, other identifying titles or degrees such as M.D. should be used.

.4	The issue of using legal terms for descriptive nouns should be considered.  The use of the word "Contractor" should not be used unless that party is legally a contractor.

.5	If the document is to be a legally binding contract the word "Contract" should be in the title.  A document entitled "Proposal" may not necessarily be a legal a contract even though signed by both parties.

.6	The word "biweekly" could be interpreted as one of two meanings: twice per week and every other week.  The same is applicable to "bimonthly."  The phrases "every other week" or "twice a week" should be used as appropriate.

.7	Numbers should be described using words and numerals, for example, ten (10).

.8	Consistent word usage should be adhered to.  If the initial reference to the subject matter in the contract is "goods", that term should be used throughout the contract, not alternating between the terms "goods" and "items".

.9	Technical terms and concepts should be clearly explained.  The owner or representative may not understand technical jargon.

.10	Every page of the contract should be initialized.

.11	Identify the parties and witnesses who sign by providing blank

lines below their signature lines for their printed names

and addresses.

### 2.3 	Site Examination

2.3.1	The Contractor shall examine the site before starting work to verify that all surfaces are properly prepared and graded.  No landscaping work shall be carried out in areas or over surfaces that are not properly prepared and graded.  See General, 1.2, Administration Recommendations for procedures for reporting improperly prepared surfaces.

### 2.4 	Supervision

2.4.1	The Contractor shall ensure competent supervision for the duration of the work on-site.

2.4.2	The person designated responsible for supervision shall ensure that the required guidelines of work, materials and safety are achieved.

2.4.3	This includes, but is not limited to, confirmation of safety codes, utility layout, records of changes, on-site coordination, scheduling and management.

2.4.4	Personnel supervising all landscape work should have post secondary education and have demonstrated expertise at supervising landscape projects.

2.5.5	The post- secondary education may include such disciplines as follow:

.1	Horticultural degree or diploma from a provincially accredited Institution

.2	Certification as a Landscape Technician under the CNLA’s Certified Horticultural Technician (CHT) landscape certification program.

### 2.5 	Scheduling

2.5.1	The Contractor shall schedule all operations to ensure optimum environmental protection, grading, planning, planting, construction, demolition, seeding or sodding operations as outlined in these Guidelines.

2.5.2	Scheduling shall be organized to ensure:

.1	A minimum duration of on-site storage of plants

.2	Minimum movement and compaction of growing medium

.3	Prompt mulching and watering operations

.4	Work schedule shall be coordinated with the Client’s schedule and other on-site trades.

.5 	Coordination and scheduling shall be such that no damage occurs to materials before or after installation.

### 2.6	Workmanship

2.6.1	The Contractor shall employ experienced personnel for all landscape and other work, and shall enforce good discipline, order and professionalism on the site at all times.

### 2.7 	Changes

2.7.1	All substantial changes in design, materials or existing conditions shall be reported both verbally and in writing, and shall be resolved in a manner not detrimental to the quality or intent of the design or the work.  (See General, 1.2, Administration Recommendations, Alternate Materials)

.1	The Owner may, without invalidating the contract, direct the company to make changes in the work.

.2	When a change causes an increase or decrease in the work, the contract price shall be increased or decreased by the application of unit prices to the adjusted proportion or in the absence of applicable unit prices, by an amount to be agreed upon between the Owner and Contractors.

### 2.8 	Testing and Certification

2.8.1	All products and materials used in the work shall be subject to testing when the Reviewer determines that testing is required to ensure that this Guideline is met.  This may include, but is not limited to, seed and seed mixes, fertilizers, manures, compost, plant tissues, mulches, growing medium and its components.

2.8.2	Testing shall be carried out by a provincially accredited, independent testing laboratory approved by the Reviewer, using commonly accepted testing methods, or methods set out in this Guideline.  Payment for testing shall be made as stated in General, 2.2.8 Field Reviews, 1.2.7

2.8.3	The testing laboratory shall make the documentation of the test results available to the Contractor, the Reviewer and Owner and shall include either:

.1  certification that the tested samples meet the requirements of this Guideline or applicable federal and provincial legislation or specifications, or:

.2  recommendations for modifying the material or product to meet this Guideline or specification.

2.8.4	The Contractor shall carry out the recommended modifications and shall submit new samples for testing if required by the Reviewer.

2.8.5	The Contractor shall only be required to modify products or materials as necessary to meet this Guideline or specification, except when the contract with the Owner requires a different product or material of equal or better quality.  (See General Requirements: Alternate Materials)

2.8.6	Samples:

.1	Samples of all materials shall be taken, handled and shipped (According to the methodological requirements of the testing labs) in such a manner that they are representative of the material or product sampled.

.2	Size of the sample is to be submitted shall be according to the amount requested by the analyzing laboratory.

.3	Samples shall be taken by the authority of the owner or designated representative and shall meet the following requirements:

.1	Commercial fertilizers:  Properly labeled bags shall constitute assurance of conformity.  Labels shall be accessible to the Reviewer on the job, and inventory taken at each delivery.  (Where large installations are involved, it may be advisable to request the Canadian Fertilizer Quality Assurance Program from the Canadian Food Inspection Agency Fertilizer Section, to check the validity of the label.  This can be done at minimum cost to the Owner or Contractor, and places full responsibility upon the supplier.)

.2	Seeds and seed mixtures: Certification by the seed supplier shall constitute assurance of conformity, except when the Reviewer has reason to verify such certification.

.3	Sand, rock, gravel and other aggregates.

.4	Soil and growing medium:

.1	Sub-samples shall be taken at the rate of one sub-sample per 1000 m2 before stripping on–site soil, or one sub-sample per 200 m3 for stockpiled on-site soil or for growing medium, to a minimum five sub-samples and maximum ten sub-samples.

.2	A well-mixed composite from 10 to 20 random locations should be sub-sampled to give the required sample size of soil to be sent to the laboratory for analysis.  Greater amounts may be needed when physical properties of the soil (such as textural classification, available moisture, nematodes or pesticide residues) are to be measured.

.3	Sub-samples shall be taken using a spade or a 25-mm sampling tube.  Sub-samples shall be thoroughly mixed to obtain a representative composite sample. Mix cores or slices together in a clean plastic container and take enough sub-sample to fill the special soil sample bag provided by the laboratory.

.4	Growing medium testing may be performed on samples provided to a testing laboratory by the supplier.  The requirement for re-testing of material may be waived if the owner or designated reviewer is satisfied that the delivered material conforms to the soil test result provided.

.5	Organic growing medium components: when required, samples of peat moss, manure, compost and other proposed organic amendments shall be supplied.

.6	Tissue samples: When required to test nutrient levels or presence and identification of pathogens.

.4	A generic collection method of a tissue sample is as follows:

.1	Use a clean plastic container as the metal may contaminate the sample.

.2	Two hundred and fifty (250) grams of lightly packed material generally provides a sufficient amount to conduct an analysis.

.3	Should plant samples have soil, dust, fertilizer, or spray residues, wash as follows:

.1	In a plastic colander, immerse the sample in cool water containing a couple of drops of Phosphate free detergent, and gently agitate for 10 seconds.

.2	Remove the colander and quickly rinse the sample under flowing pure water.

.3	Either air-dry or blot-dry samples and ship as soon as possible in perforated bags to allow air movement and a degree of drying while in transit.

.4	Do not include roots with samples for nutrient analysis unless required.

.5	Samples in the quantities and conditions set out in the Guideline shall be provided to the Reviewer for testing within an agreed to reasonable time for the request for samples

.6	The Reviewer may, at their discretion, waive the requirement of testing for each particular project.

### 2.9 	Field Reviews, Acceptance

2.9.1	Field review procedures are recommended in General, 1.2 Administration Recommendations.

2.9.2	The Reviewer shall have access to the work site at all reasonable times for ensuring compliance with this Guideline.

2.9.3	The Reviewer shall not interfere with the Contractor’s control and management of the work and contractor’s forces.

2.9.4	The Contractor shall give reasonable notice when the work will be ready for field reviews in order to avoid delays. Field reviews and reports shall be timed to avoid unnecessary delays in the execution of the work.

2.9.5	Conditions for Acceptance of work are shown in the General part of each section.   Acceptance and turnover procedures are recommended in General, 1.2, Administration Recommendations.

### 2.10 	Guarantee/Warranty Maintenance

2.10.1	The customary one-year guarantee period for the construction industry is accepted as the guideline for landscape work.  The Contractor should guarantee all materials and workmanship for a period of one (1) full year from Acceptance, unless specified otherwise in the contract with the Owner.

2.10.2	If at any time prior to one year (or specified warranty/guarantee period) after the actual delivery date of the equipment (or completion of any work) any part of the equipment or work becomes defective or is deficient or fails due to defect in design, material or workmanship, or otherwise fails to meet the requirements of the contract, then the company, upon request, shall make good of every such defect, deficiency or failure without costs for parts and/or equipment both ways between company’s factory or repair depot and the point of use.

2.10.3	The Landscape Guideline can never override provisions of a contract; however, there are usually three distinct periods to be considered:

.1	Before Acceptance and takeover by Owner: Generally, the Contractor maintains and is solely responsible for the plant material.

.2	During One-Year Warranty Period: In most cases the Owner is responsible for maintenance and protection, unless the contract includes one-year maintenance by contractor.  Contractor is responsible to make good for faulty products or workmanship.

.3	After the Warranty Period: The Owner is responsible, unless otherwise stated.

2.10.4	Guarantee periods greater than one year for specific works, notably large trees, interlocking paving and decking should be clearly noted in the working documents or specifications.

2.10.5	The guarantee includes replacing all plants (and supplying required labour) that are determined by the Reviewer to be dead or failing at the end of the guarantee period.  Plant replacements shall be made at the next appropriate season, and the conditions of the guarantee shall apply to all replacement plants for one full growing season, unless otherwise stated or the below conditions are applicable:

.1   The guarantee should not apply to plants or other products damaged after Acceptance by causes beyond the Contractor’s control, such as inadequate maintenance by others, vandalism or abuse.  The Contractor is considered responsible for the work until Acceptance.  After Acceptance, unless otherwise specified, the Owner is considered responsible for the work, and for proper maintenance, repairs, and plant replacements.

.2   In circumstances where the landscape contractor responsible for the guarantee feels the owners are not providing adequate maintenance, the landscape contractor shall inform the owner(s) in writing of the limitations to the guarantee.  In the case of a project subject to municipal development and/or building permits the notice of limitations to the guarantee must be copied to all participants in the original contract and contract review.  A reasonable notice and period of time shall be allowed to permit the owners to respond.

.3   In circumstances where the owner feels the landscape contractor is not providing adequate maintenance, the owner should inform the landscape contractor in writing of the requirements of the guarantee.  In the case of a project subject to municipal development and/or building permits, the notice of requirements of the guarantee must be copied to all participants in the original contract and contract review.  A reasonable period of time and notice shall be allowed to permit the landscape contractor to respond.

2.10.6	The guarantee cannot be considered valid unless it can be proven that the requirements of Chapter 17  Establishment Maintenance has been carried out to a degree acceptable to the Reviewer.  It is therefore recommended that the Owner should follow the recommendations of Chapter 16.

### 2.11  	Environmental Protection

(See also Chapter 3 Site Preparation and Protection of Existing Elements)

2.11.1   Environmental damage shall be avoided by ensuring that all construction and maintenance operations are carefully planned and scheduled.  Areas that are sensitive or that pose potential problems shall be noted and schedules and work methods shall be prepared and executed accordingly.

2.11.2   Soil stripping operations shall be carried out in such a manner as to avoid release of silt or sediment into any stream or storm drains or other water bodies.  Retention ponds, siltation, screens, dikes etc. shall be installed where necessary to prevent rapid site runoff into watercourses, as directed by the civil engineer, professional consultant or environmental authority.

2.11.3   Stockpiled soil(s) shall not be placed in depressed areas where natural drainage or storm water could pond or erode these materials during inclement weather.

2.11.4   Temporary erosion control measures shall be provided to prevent excessive runoff on to adjacent sites or watercourses, or where a soil erosion hazard exists.  Measures may include mulching, diking, ponding, and terracing or other means to reduce surface water flow.

2.11.5   Appropriate measures shall be taken to ensure that no spillage of fuels or toxic materials, occur, and where the use of such materials are required or produced, to ensure that adequate containment facilities and clean-up equipment are utilized.

2.11.6   No toxic materials, fertilizers, or fuels or waste materials shall be:

.1	Dumped into watercourses or any other water body either on or off the work site.

.2	Stored adjacent to watercourses or storm drains in a location where spillage/leakage could result in seepage into a watercourse or storm drains.

2.11.7 	All toxic wastes and other construction material shall be disposed of in accordance with all municipal, provincial and federal regulations.

### 2.12	Site Protection

(See also Chapter 3 Site Preparation and Protection of Existing Elements)

2.12.1	All new and existing plants, site services, curbs, paving, structures, finishes and all other features shall be protected against damage during the work.  Damage shall be reported (see 2.16) and shall be completely repaired to the satisfaction of the Authority or Owner.

2.12.2	Preservation of Existing Vegetation

.1   Existing trees and plants should be protected except where otherwise shown in the working documents or where designated for removal by appropriate qualified professionals.

.2   Appropriate means of protecting existing trees should be used throughout all phases of construction, including those stated in Chapter 3, Site Preparation and Protection of Existing Site Elements.

2.12.3	The onus shall be upon the contractor or bidder to investigate the project site and before the tendering of all the physical and working conditions and administrative practices.

2.12.4	The establishment of boundaries for tree protection zones, and all construction work near existing trees that are to be retained, should be directed and supervised by a professional consultant such as an ISA Certified Arborist.

### 2.13  	Safety

2.13.1	The Contractor shall comply with all applicable laws, bylaws, rules, regulations and orders from any public authority having jurisdiction for the safety of persons or property or to protect them from damage, injury or loss.

2.13.2	The Contractor shall erect and maintain, as required by existing conditions and progress of the work, all reasonable safeguards for safety and protection, as required by the Occupational Health and Safety Council, the Workplace Safety Insurance Board and other regulations and legislation.

2.13.3	The Contractor shall provide sufficient signage, barricades, safety guards, and/or warning devices for purposes of controlling traffic and pedestrians whenever necessary for the protection of persons and property.

2.13.4	The Company shall be responsible for being cognizant of all governing regulations including those established by the corporation, related to employee health and safety.  The company shall keep all employees and subcontractors informed of such regulations.

### 2.14 	Laws and Regulations

2.14.1	The Company shall comply with relevant federal, provincial and municipal statutes, regulations and by-laws pertaining to the work and its performance.

2.14.2	The Company shall be responsible for ensuring similar compliance by its suppliers and subcontractors.

2.14.3	The contract shall be governed by and interpreted in accordance with the laws of the province of Ontario.

### 2.15 	Chemicals

.1	Handling and application of all chemicals, including but not limited to pesticides (which include but are not limited to: herbicides, fungicides and insecticides) shall be done solely by persons legally licensed or certified to do so under provincial and federal legislation.

.2	The use, handling and disposal of chemicals shall comply with all applicable legislation and regulations, including, but not limited to, the federal Pest Control Products Act, Fisheries Act, and Food and Drugs act; and the provincial Pesticide Control Act, Wildlife Act, Weed Control Act, Plant protection Act, and Waste Management Act, Transportation of Dangerous Goods Act, as well as any municipal or regional district legislation.  (See Legislation Appendix “B”).

### 2.16 	Reporting Damage

2.16.1	Notification of danger or damage to property, persons, utilities, site features or the environment shall be given at once, verbally, and in writing, to the Authority/Owner and to the appropriate public agencies or authorities responsible for the safety and repair of such property such as public utilities or for the protection of the environment.

### 2.17 	Water

2.17.1	Water used for the work shall be free from any organic or chemical contaminants detrimental to healthy plant growth.

2.17.2	Planning, scheduling and execution of the work shall include measures to ensure an adequate supply of water for landscape and construction usage purposes in adequate amounts and also at adequate pressures for satisfactory irrigation of all plant material.

2.17.3	Planning of the work shall include provision of a satisfactory means of water distribution.  Such means include, but are not limited to, automatic sprinkler systems, drip systems, hose bibs and connection points, and truck-mounted water tanks.

### 2.18	 Insurance

2.18.1	Unless other provisions are agreed to, the Contractor shall obtain, provide, maintain and pay for insurance.  Evidence of insurance shall be signed by the insurer or his authorized representative and shall be submitted on the Certificate of Insurance for the duration of the work, providing at least the following coverage for the following categories of risk.

.1   Comprehensive General Liability Insurance protecting the Owner, the Contractor, subcontractors, and their respective agents or employees against damage arising from personal injury or death and against claims for property damage that may arise directly or indirectly out of the operations of the Contractor, their subcontractors or employees.  The amount of coverage should be not less than $2,000,000 inclusive for any one occurrence.  This policy shall contain a guideline cross liability clause, and shall cover all liability arising out of products, whether manufactured or supplied by the Contractor, contingent employer’s liability and liability assumed by the Contractor under and applicable to the contract for the work.

.2   Automobile Insurance on the Contractor’s owned and non-owned vehicles, protecting the Contractor and the Owner against damages arising from bodily injury or death and against claims for property damage arising out of their use on the operations of the Contractor and their subcontractors.  The amount of coverage should be not less than $2,000,000 inclusive for any one occurrence.

.3	The Occupational Health and Safety Act

(Revised Statutes of Ontario 1980, Chapter 321 and Regulations for Construction Projects, Ontario Reg.213/91)

This Contract is deemed to be an individual “Project” for the purposes of the Occupational Health and Safety Act and the regulations made thereunder and the Contractor to whom the Contract is awarded unequivocally acknowledges that he is the “Contractor” as defined in the said “Act” of the “Project” and shall carry out all of the obligations and shall bear all of the responsibilities of the contractor as set out in the said Act and Regulations.

.4	A certificate from the Workplace Safety Insurance Board shall be provided prior to the commencement of work indicating all payments by the Contractor to the owner in conjunction with the subject contract have been made, and that the corporation will not be liable to the board for future payments in connection with the company’s fulfillment of the contract.